## Slide 1
ARUNA · smart home biodigester
01
RESEARCH & DEVELOPMENT · ENVIRONMENTAL ENGINEERING
ARUNA
Kinetic-based design of an IoT-enabled household anaerobic digester for food waste
Anaerobic Recycling and Upcycling of Nutrient-rich food wAste: sized from mass balance and Gompertz kinetics, instrumented with NDIR methane sensing and safety interlocks.
SDG 7.1
SDG 11.6
SDG 12.3
SDG 13.2
[Team name] · [Supervisor] · [Institution] · 2026

## Slide 2
02 · BACKGROUND
Food waste is Indonesia's largest organic waste stream.
ARUNA · smart home biodigester
02
53 kg
household food waste per capita per year
UNEP (2024)
14.7 Mt
household food waste per year, Indonesia
UNEP (2024)
≈40%
of municipal solid waste is food waste
SIPSN KLHK (2023)
1.7 Gt
CO₂e from food loss & waste, 2000–2019
Bappenas (2021)
Why anaerobic digestion?
Property of food waste | Typical value | Source
Total solids (TS) | 23–27 % | Xu et al. (2018)
Volatile solids (VS/TS) | 90–95 % | Xu et al. (2018)
Biochemical CH₄ potential | 330–490 mL CH₄/g VS | Zhang et al. (2007)
Theoretical (Buswell) | ≈ 643 mL CH₄/g VS | Buswell & Mueller (1952)
Research questions
● RQ1 What digester volume, OLR and HRT keep household food-waste digestion stable?
● RQ2 How much biogas, cooking time and avoided CO₂e can one unit deliver?
● RQ3 Can sensor feedback make the process usable for non-experts (SUS ≥ 68)?
Sources: UNEP Food Waste Index Report 2024; SIPSN KLHK 2023; Bappenas 2021 FLW study; Zhang et al. 2007, Bioresour. Technol. 98:929; Xu et al. 2018, Bioresour. Technol. 247:1047.

## Slide 3
03 · STATE OF THE ART
Current options trade energy, space or visibility.
ARUNA · smart home biodigester
03
Approach | Footprint / scale | Input | Energy balance | Monitoring | Main limitation
Electric food recycler (Lomi) | countertop | food scraps | consumes 0.6–1.0 kWh/cycle | app | no energy recovery
HomeBiogas 2 | 2.1 × 1.15 m, 2.0 m³ | 4 L FW + 4 L water/d | up to 2 h cooking/d | visual | outdoor, 2.4 m² footprint
Fixed-dome digester (BIRU) | masonry, outdoor | livestock manure | household cooking gas | none | needs manure; 25,157 units (2021)
IoT digester research | pilot / lab | mixed organics | measured, not productised | ESP32: T, pH, CH₄, H₂S | not a household device
ARUNA | 0.44 × 0.44 m, 100 L | 1.5 kg FW + 1.5 L water/d | ≈43 min cooking/d (predicted) | NDIR CH₄, pH, T, level + interlocks | to be field-validated
Research gap
No household option combines food-waste input, energy recovery, indoor footprint and real-time process monitoring. Low-cost MQ-type gas sensors (300–10,000 ppm) cannot quantify biogas CH₄ (50–70 % vol); an NDIR sensor (0–100 % vol) is required.
Sources: Lomi (2024) energy use; HomeBiogas (2024) HB2 specifications; ESDM/Hivos BIRU (2021); Prasetyono et al. 2026, J. Mechatron. Electr. Power Veh. Technol. 17(1):29; Rajendran et al. 2012, Energies 5:2911; Winsen MQ-4 & MH-440D datasheets.

## Slide 4
04 · SOLUTION
Shred, stir, digest, measure: three outputs.
ARUNA · smart home biodigester
04
1
Biogas
214 L/d · 1.3 kWh/d
2
Liquid digestate
N-rich fertilizer, dilute 1:10
3
Solid digestate
compost drawer
SDG 7.1
clean cooking fuel ≈ 3.0 kg LPG-eq/month
SDG 11.6
0.55 t/yr diverted from municipal waste
SDG 12.3
food waste valorised at source
SDG 13.2
0.72 t CO₂e/yr avoided (potential)
H1 At OLR ≤ 3.4 kg VS/m³·d and HRT ≈ 34 d: CH₄ ≥ 50 %, ≥ 0.30 m³ CH₄/kg VS, FOS/TAC < 0.4. H2 SUS ≥ 68.
Sources: Design calculation (this work) using Zhang et al. 2007; Xu et al. 2018; IPCC 2006 Vol. 5 Ch. 3; IPCC AR5 GWP100 = 28; UN A/RES/70/1 (SDG targets).

## Slide 5
05 · THE PRODUCT
A 0.19 m² digester with a digital twin.
ARUNA · smart home biodigester
05
Hardware | Value
Footprint × height | 44 × 44 × 112 cm
Working volume | 100 L
Nominal / peak load | 1.5 / 3.0 kg FW/d
HRT / OLR | 34 d / 3.4 kg VS/m³·d
Controller | ESP32-S3 (Wi-Fi, BLE)
Process sensors | T, pH, NDIR CH₄, level, mass
Safety | MQ-4 leak alarm, valve
Software | Implementation
Telemetry | 15-min sampling → Firebase RTDB
Interface | PWA, live at aruna-id.web.app
Guidance | interlock alerts + AI educator
Setup | BLE provisioning, offline
Sources: This work (3D model & live app); Espressif ESP32-S3 datasheet; Google Firebase Realtime Database documentation.

## Slide 6
06 · THE HARDWARE
Gravity-fed layout, instrumented for process control.
ARUNA · smart home biodigester
06
7″ panel + ESP32-S3
Twin-shaft shredder
Load cell (HX711)
Stirrer, 5 min / 2 h
Liquid digestate tap
Solid digestate drawer
Parameter | Sensor | Range | Accuracy / role
Temperature | DS18B20 | −55–125 °C | ±0.5 °C
CH₄ in biogas | NDIR MH-440D | 0–100 % vol | T90 < 30 s
CH₄ leak | MQ-4 | 300–10,000 ppm | alarm 10 % LEL
pH | glass probe | 0–14 | 3-pt calibration
Level | ultrasonic | 0–100 % fill | ≈ ±1 cm
Input mass | load cell + HX711 | 0–5 kg | 24-bit ADC
Gas volume | diaphragm meter | L/d | reference
Safety & process interlocks
leak > 5,000 ppm → close valve · pH < 6.5 → pause feeding · T < 30 °C → insulation alert · level > 90 % → harvest prompt
Sources: Maxim/Analog Devices DS18B20 datasheet; Winsen MH-440D (NDIR, 0–100 % vol) & MQ-4 (300–10,000 ppm) datasheets; CH₄ LEL 5 % vol.

## Slide 7
07 · THE SOFTWARE
From raw signals to plain-language decisions.
ARUNA · smart home biodigester
07
Status
Trends + ideal band
AI educator
Sources: This work (rule-based controller, live PWA). Rule thresholds: pH 6.5–7.5 and FOS/TAC < 0.4 (Chen et al. 2008, Bioresour. Technol. 99:4044; Liu et al. 2021, Appl. Sci. 11:11843).

## Slide 8
08 · USE CASE
One day of operation, quantified.
ARUNA · smart home biodigester
08
1
Feed
1.5 kg FW + 1.5 L water; weighed & shredded
2
Digest
OLR 3.4 kg VS/m³·d, stir 5 min / 2 h
3
Monitor
15-min telemetry; alert if pH < 6.5
4
Fertilize
liquid digestate diluted 1:10
5
Cook
214 L biogas ≈ 43 min at 0.30 m³/h
Sources: Design calculation (this work); stove demand 0.2–0.45 m³/h (SSWM/Akvopedia, Biogas combustion, 2019).

## Slide 9
09 · RESEARCH METHOD
R&D (4D model) with quantitative exit criteria.
ARUNA · smart home biodigester
09
Mass balance
OLR = F·TS·(VS/TS) / Vw HRT = Vw / Q
Kinetics (Gompertz)
M(t) = P·exp{−exp[(Rm·e/P)(λ − t) + 1]}
Theoretical CH₄ (Buswell)
CcHhOoNn + H₂O → CH₄ + CO₂ + NH₃
Energy & cooking
E = VCH4 · 35.8 MJ/m³ ; tcook = Vbiogas / qstove
Avoided landfill CH₄ (IPCC)
W · DOC · DOCf · MCF · F · 16/12 · (1 − OX)
Experiment | Design | Standard / method | Output
BMP assay | ISR ≥ 2, 37 °C, triplicate | VDI 4630 | P, Rm, λ
Semi-continuous | OLR 2.0 / 3.4 / 4.5 × 3 reps, 2 HRT | APHA 2540 G; FOS/TAC | yield, stability
Field test | [n] households × 30 d | telemetry + logbook | CH₄ %, L/d, kg/d
Usability | post-test questionnaire | SUS (Brooke 1996) | score 0–100
● Kinetics: non-linear least squares, R², RMSE
● Comparison: one-way ANOVA + Tukey, α = 0.05
● Biodegradability: BMP(exp) / BMP(theoretical)
Sources: Thiagarajan et al. 1974; Buswell & Mueller 1952, Ind. Eng. Chem. 44:550; Zwietering et al. 1990, Appl. Environ. Microbiol. 56:1875; VDI 4630 (2016); APHA 2540 (2017); Brooke 1996.

## Slide 10
10 · FIELD TESTING
Measurement plan with acceptance criteria.
ARUNA · smart home biodigester
10
ILLUSTRATIVE DATA · replace with field results
Parameter | Instrument / method | Frequency | Acceptance | Basis
Temperature | DS18B20 | 15 min | 30–38 °C | Weiland (2010)
pH | calibrated probe | 15 min | 6.8–7.5 | Chen et al. (2008)
FOS/TAC | two-point titration | weekly | < 0.4 | Liu et al. (2021)
CH₄ content | NDIR + [ref. analyser] | continuous | ≥ 50 % vol | Xu et al. (2018)
Biogas volume | diaphragm gas meter | daily | ≥ 171 L/d | this work (−20 %)
TS / VS | APHA 2540 G | weekly | VS removal ≥ 70 % | Mata-Alvarez (2000)
Digestate N, P, K | lab analysis | end of cycle | [standard] | national fertilizer standard
Usability | SUS | end of test | ≥ 68 | Bangor et al. (2009)
Rendered scenario; replace with field photos.
Sources: Weiland 2010; Chen et al. 2008; Liu et al. 2021, Appl. Sci. 11(24):11843; Xu et al. 2018; Mata-Alvarez et al. 2000, Bioresour. Technol. 74:3; APHA 2540 (2017); Bangor et al. 2009, J. Usability Stud. 4:114.

## Slide 11
11 · RESULT & DISCUSSION
Design predictions against the literature.
ARUNA · smart home biodigester
11
PREDICTED FROM DESIGN CALCULATION · measured data pending
Parameter | Household of 4 | Nominal | Peak
Input (kg FW/d) | 0.58 | 1.5 | 3.0
OLR (kg VS/m³·d) | 1.3 | 3.4 | 6.8
HRT (d) | 88 | 34 | 17
Biogas (L/d) | 83 | 214 | 428
Cooking (min/d) | 17 | 43 | 86
LPG-eq (kg/month) | 1.2 | 3.0 | 6.0
Avoided (t CO₂e/yr) | 0.28 | 0.72 | 1.44
● Biodegradability ≈ 61 %: BMP 390 vs Buswell 643 mL CH₄/g VS, within reported food-waste range (Zhang et al., 2007).
● Stability: nominal OLR 3.4 is within stable ranges; peak OLR 6.8 at HRT 17 d risks VFA accumulation → pH interlock (Chen et al., 2008).
● Scale: a household of 4 yields ≈ 17 min/d; nominal load fits extended families or small eateries.
Sources: Design calculation (this work); Gompertz parameters from literature ranges, to be fitted (Zwietering et al. 1990); Zhang et al. 2007; Chen et al. 2008; UNEP 2024 (53 kg/cap/yr).

## Slide 12
12 · FUTURE DEVELOPMENT
From prototype to verified impact.
ARUNA · smart home biodigester
12
1
0–6 months · Validate
● BMP + semi-continuous tests; fit P, Rm, λ
● calibrate NDIR vs gas analyser
2
6–12 months · Optimise
● co-digestion to C/N 20–30
● H₂S scrubber; insulation for T < 25 °C
3
12–36 months · Scale
● on-device AI waste recognition
● MBG school-kitchen pilots with MRV
Sources: Sensitivity analysis (this work); C/N 20–30 and H₂S removal (Weiland 2010, Appl. Microbiol. Biotechnol. 85:849; Mata-Alvarez et al. 2000).

## Slide 13
13 · CONCLUSION
Answers to the research questions.
ARUNA · smart home biodigester
13
RQ1
A 100 L digester at OLR 3.4 kg VS/m³·d and HRT ≈ 34 d is predicted to be stable for 1.5 kg/d; peaks above ≈ 3 kg/d require pausing.
RQ2
≈ 214 L biogas/d → ≈ 43 min cooking, ≈ 3.0 kg LPG-eq/month and ≈ 0.72 t CO₂e/yr avoided.
RQ3
NDIR sensing, rule-based interlocks and app guidance close the monitoring gap; SUS to be measured.
Live prototype app aruna-id.web.app
Values are design predictions; measured results will replace them after testing.
Sources: This work; IPCC 2006 Vol. 5 Ch. 3 (FOD defaults); IPCC AR5 (GWP100 = 28).

## Slide 14
14 · REFERENCES
Literature and data sources.
ARUNA · smart home biodigester
14
1. APHA (2017). Standard Methods for the Examination of Water and Wastewater, 23rd ed., Method 2540.
2. Appels, L. et al. (2008). Prog. Energy Combust. Sci. 34(6), 755–781. doi:10.1016/j.pecs.2008.06.002
3. Bangor, A., Kortum, P., Miller, J. (2009). J. Usability Stud. 4(3), 114–123.
4. Bappenas (2021). Food Loss and Waste in Indonesia. Ministry of National Development Planning.
5. Brooke, J. (1996). SUS: a 'quick and dirty' usability scale. Usability Evaluation in Industry, 189–194.
6. Buswell, A. M., Mueller, H. F. (1952). Ind. Eng. Chem. 44(3), 550–552. doi:10.1021/ie50507a033
7. Chen, Y., Cheng, J. J., Creamer, K. S. (2008). Bioresour. Technol. 99(10), 4044–4064. doi:10.1016/j.biortech.2007.01.057
8. ESDM (2021). Strategi pengembangan biogas menuju target 1 juta biodigester. Ditjen EBTKE.
9. HomeBiogas (2024). HomeBiogas 2 product specifications. homebiogas.com
10. IPCC (2006). Guidelines for National GHG Inventories, Vol. 5 Waste, Ch. 3.
11. IPCC (2014). Climate Change 2014: Synthesis Report (AR5).
12. KLHK (2023). SIPSN: Komposisi sampah. sipsn.menlhk.go.id
13. Liu, X. et al. (2021). Appl. Sci. 11(24), 11843. doi:10.3390/app112411843
14. Lomi (2024). How much energy does Lomi use? lomi.com
15. Mata-Alvarez, J., Macé, S., Llabrés, P. (2000). Bioresour. Technol. 74(1), 3–16. doi:10.1016/S0960-8524(00)00023-7
16. Prasetyono, S. et al. (2026). J. Mechatron. Electr. Power Veh. Technol. 17(1), 29–38. doi:10.55981/j.mev.2026.1352
17. Rajendran, K. et al. (2012). Energies 5(8), 2911–2942. doi:10.3390/en5082911
18. SSWM / Akvopedia (2019). Biogas combustion. sswm.info
19. Thiagarajan, S., Semmel, D. S., Semmel, M. I. (1974). Instructional Development for Training Teachers of Exceptional Children. Indiana Univ.
20. UNEP (2024). Food Waste Index Report 2024. Nairobi.
21. VDI 4630 (2016). Fermentation of organic materials. Verein Deutscher Ingenieure.
22. Weiland, P. (2010). Appl. Microbiol. Biotechnol. 85(4), 849–860. doi:10.1007/s00253-009-2246-7
23. Winsen (n.d.). MH-440D NDIR CH₄ sensor; MQ-4 gas sensor datasheets.
24. Xu, F. et al. (2018). Bioresour. Technol. 247, 1047–1058. doi:10.1016/j.biortech.2017.09.020
25. Zhang, R. et al. (2007). Bioresour. Technol. 98(4), 929–935. doi:10.1016/j.biortech.2006.02.039
26. Zwietering, M. H. et al. (1990). Appl. Environ. Microbiol. 56(6), 1875–1881. doi:10.1128/aem.56.6.1875-1881.1990